## Slide 1: Maintenance of Bleachers and Light Poles Texas Gulf Coast Maintenance and Operations Meeting January 11, 2018
Joanna Monge, P.E.
Senior Project Engineer

## Slide 2: What do we want to know?
Who?
What?
When?
Where?
Why?
How?
What?
Why?
When?
Who?
How?
Where?

## Slide 3: What?
Bleachers
Interior, telescopic
Exterior, grandstand
Portable, free standing
Aluminum
Steel
Wood

## Slide 4: What?
Light Poles
Parking Lots
Stadium/Athletic/High Mast/Monopole

## Slide 5: What?
ICC 300: Standard for Bleachers, Folding, and Telescopic Seating, and Grandstands
AASHTO LTS-5: Standard Specifications for Structural Supports for Highway Signs, Luminaires, and Traffic Signals
Applicable Standards
ICC – International Code Council
AASHTO – American Association of State Highway and Transportation

## Slide 6: Why?
  Safety
  “An ounce of prevention is better than a pound of cure.”
  Properly designed and maintained bleachers and light poles will remain in service for a long time
  Cost savings

## Slide 7: New Bleachers and Light Poles
Engage licensed professional engineers and architects
Designs are signed and sealed by professional engineers
In accordance with:
  ICC 300: Standard for Bleachers, Folding, and Telescopic Seating, and Grandstands
  AASHTO LTS-5: Standard Specifications for Structural Supports for Highway Signs, Luminaires, and Traffic Signals

## Slide 8: When?
Bleachers
  ICC 300 – annual
  Quarterly by maintenance team
  Biannually by third-party inspectors
Light Poles
  AASHTO LTS-5 – annual
  Quarterly by maintenance team
  Biannually by third-party inspectors
Day-to-day
YEAR
Quarter
Quarter
Quarter
Quarter
Biannual
Biannual

## Slide 9: Who?
Maintenance personnel
Manufacturer’s warranty
Third-party material testing and inspection companies
  Licensed/qualified personnel (engineers, architects) with bleachers and light pole engineering experience
  AWS certified welding inspectors for non-destructive testing

## Slide 10: How?
Visual assessment
  Aerial working platforms
  Drone cameras
  Borescope
Non-destructive testing
  Coating thickness test (galvanized/peeling paint)
  Magnetic particle testing for cracks in welds
  Ultrasonic thickness testing for material section/thickness loss due to corrosion

## Slide 11: Where? Bleachers – Seating and Steps

## Slide 12: Where? Bleachers – Connections and Fasteners

## Slide 13: Where? Bleachers – Lateral stabilizing elements

## Slide 14: Where? Bleachers – Handrails

## Slide 15: Where? Bleachers – Mechanisms

## Slide 16: Where? Light Poles – Pole Shaft and Fixtures

## Slide 17: Where? Light Poles – Handholes

## Slide 18: Where? Light Poles – Base Plates and Covers

## Slide 19: Where? Light Poles – Anchor Bolts and Fasteners

## Slide 20: Where? Light Poles – Welds

## Slide 21: Data Asset Management – Out with the Old
What do you do with the information?
  Field evaluation forms
  Photos
Transfer data to:
  Spreadsheets
  Photo Logs
  Cross-referencing
Tedious and time-consuming
  Maintain archive records
  Growing paperwork

## Slide 22: Data Asset Management – In with the New
Terracon’s updated approach
Online cloud storage-based data management system
  Aerial maps (Bing, Google, Eagleview, etc.)
  Tag facilities and assets
  Access via mobile app or desktop
  GPS coordinates
  Real-time updates

## Slide 23: Data Asset Management – Mobile Data Input

## Slide 24: Data Asset Management – District View (Desktop)

## Slide 25: Data Asset Management – Facility View (Desktop)

## Slide 26: Data Asset Management – Asset Window (Desktop)

## Slide 27: Data Asset Management – Online Data Export (Inventory)
Facility Name | General Location | Asset Identifier | Bleacher Type | Frame/Structural Material Type | Frame/Structural Coating System | Number of Rows | Seating Material Type | Tread Area Material Type | Tread Area Coating (if applicable) | Seating Area Coating (if applicable)
HS | FOOTBALL | FOOTBALL-B-1 | FIX | STEEL | GALV | 33 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-2 | FIX | STEEL | GALV | 33 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-3 | FIX | STEEL | GALV | 33 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-4 | FIX | STEEL | GALV | 33 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-5 | FIX | STEEL | GALV | 33 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-6 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-7 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-8 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-9 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-10 | FIX | STEEL | GALV | 30 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-11 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-12 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-13 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL
HS | FOOTBALL | FOOTBALL-B-14 | FIX | STEEL | GALV | 18 | AL | AL | ANO | MILL

## Slide 28: Data Asset Management – Online Data Export (Condition Assessment)
Asset Identifier | Assessment Date | Overall Condition of Asset | Structure/Frame Condition | Structure/Frame Coating Condition | Seating Area Condition | Seating Area Coating Condition | Tread/Step Area Condition | Tread/Step Area Coating Condition | Handrail Condition | Lateral Stabilizing Element Condition | Notes | Comments
HS-FOOTBALL-B-1 | 9/20/2017 19:54 | GOOD | GOOD | GOOD | GOOD | GOOD | FAIR | FAIR | GOOD | GOOD |  | 
HS-FOOTBALL-B-2 | 9/20/2017 19:39 | GOOD | GOOD | GOOD | GOOD | FAIR | FAIR | FAIR | NA | GOOD | Loose metal guard. Loosened metal stair cap | 1. Perform maintenance on slip guard.
HS-FOOTBALL-B-3 | 9/20/2017 19:21 | GOOD | GOOD | GOOD | GOOD | GOOD | FAIR | FAIR | GOOD | GOOD |  | 1. Perform maintenace on trade area coating.
HS-FOOTBALL-B-4 |  | GOOD | GOOD | GOOD | GOOD | GOOD | FAIR | FAIR | GOOD | GOOD |  | 1. Perform maintenace on trade area coating.
HS-FOOTBALL-B-5 | 9/20/2017 18:09 | GOOD | GOOD | GOOD | GOOD | GOOD | FAIR | FAIR | GOOD | GOOD | Anchor bolts in good condition except one bolt and nut anchor on column line 15 which has rust. | 1. Replace the bolt and nut at column line 15
HS-FOOTBALL-B-6 | 9/20/2017 16:44 | GOOD | GOOD | GOOD | GOOD | GOOD | GOOD | GOOD | GOOD | GOOD |  | 
HS-FOOTBALL-B-7 | 9/20/2017 16:30 | GOOD | GOOD | GOOD | FAIR | FAIR | GOOD | FAIR | GOOD | GOOD | Non structural issue on bleachers. Lots of dirt and discoloration. | 
HS-FOOTBALL-B-8 | 9/20/2017 16:19 | GOOD | GOOD | GOOD | GOOD | GOOD | GOOD | FAIR | GOOD | GOOD |  | 
HS-FOOTBALL-B-9 | 9/20/2017 16:00 | GOOD | GOOD | GOOD | FAIR | GOOD | GOOD | GOOD | GOOD | GOOD | First row of seating is missing a connection between seating causing it to be unsafe. | 1. Repair the first row of seating.
HS-FOOTBALL-B-10 | 9/20/2017 15:43 | GOOD | GOOD | GOOD | GOOD | GOOD | FAIR | FAIR | GOOD | GOOD | Thread and seating support exhibiting early signs of rust. | 1. Perform maintenace on trade area coating.
HS-FOOTBALL-B-11 | 9/20/2017 15:26 | GOOD | GOOD | GOOD | GOOD | GOOD | FAIR | FAIR | GOOD | GOOD | Early signs of rusting present on thread area. | 1. Perform maintenace on trade area coating.
HS-FOOTBALL-B-12 | 9/20/2017 15:10 | GOOD | GOOD | GOOD | FAIR | FAIR | FAIR | FAIR | GOOD | GOOD | Seating and thread are issues are non structural. Fading and debris observed on seating areas. | 
HS-FOOTBALL-B-13 | 9/20/2017 14:57 | GOOD | GOOD | GOOD | FAIR | GOOD | FAIR | FAIR | FAIR | GOOD | Thread area showing signs of wear and tear. | 
HS-FOOTBALL-B-14 | 9/20/2017 14:46 | GOOD | GOOD | GOOD | FAIR | FAIR | FAIR | FAIR | GOOD | GOOD |  | 1. Resurface and repaint the bleacher observed and wide spread issue of rusting.

## Slide 29: Repairs – Before and After
Deficiencies have been identified.
Develop a repair plan
  Often may be undertaken by maintenance personnel (missing bolts and washers, cleaning and repainting, etc.)
If extensive repair or strengthening is required, engage the services of a professional engineering firm.
After repairs are completed, perform post-repair assessment to ensure repairs were done correctly.
Continue with regular assessments on a consistent basis.

## Slide 30
Joanna Monge, P.E. 11555 Clay Road Phone: 713-690-8989
Senior Project Engineer Suite 100 Fax: 713-690-8787
joanna.monge@terracon.com Houston, Texas 77043 terracon.com
QUESTIONS?